Towards a conceptual framework for the design of intelligent packaging services in print and cross-media: the role of decision support systems

Spyridon Nomikos, Panayiotis Koutsabasis, Jenny S. Darzentas, Thomas Spyrou, John Darzentas
Department of Product and systems Design Engineering, University of the Aegean, Hermoupolis, 84100 Syros, Greece, 
{nomic; kgp; jennyd; tsp; idarz}@aegean.gr

Abstract: Packaging is currently at the centre of an intensive research effort that is being carried out regarding new technologies that integrate digital data in and on a package. This effort has been fuelled by recent developments in electronics technology, materials and processes that offer the potential to create inexpensive ways to produce packaging that can carry disposable digital machine readable data regarding many operations from logistics and inventory data, to contents and instructions for use, leading to greater automation in the operations. The goal of this paper is to identify a conceptual framework that can assist the understanding of the related emerging requirements (that are related to both print and cross-media) by investigating the role of decision support systems to the multidisciplinary aspects of the design of intelligent packaging services.

Keywords: intelligent packaging design, print media, cross media, conceptual framework, decision support systems

…………….

……………..

………………

Table 1: Industrial printing technologies for packaging

| Method | Printing forms (Plate/Cylinder) | Productivity | Material |
| --- | --- | --- | --- |
| OFFSET. Chemical printing Sheet/web | Metal | little large -extra large | paper/ cardboard/ self-adhesive/ metal/ plastic |
| FLEXOGRAPHY Relief printing | Photopolymer Roll /sleeve | Large/ extra large | paper/plastic films, hdpe, ldpe, |
| GRAVURE- and Intaglio printing | Roll copper Flat copper | Extra large little | Plastic ,films, nylon, polyester /foil aluminum Paper-paper board |
| SILK SCREEN Ι (flat bed/Frame) | Frame metal-plastic screen | little | All the surfaces compatible with the ink |
| SILK SCREEN ΙΙ(cylinder) | Cylindrical form, plastic metal-screen | mediocre | All the surfaces compatible with the ink |
| PAD Printing/2d/3,dimensions, Printing surfaces | Intaglio /elastic silicone of small size | little | Various materials 3d/ surfaces |
| DIGITAL PRINTING Electrophotography, a. liquid toner b. dry toner | Digital File | little / mediocre | Paper/cardboard/sticker plastic |
| DIGITAL PRINTING Thermal, (liquid/bubble) | Digital File | little / mediocre | Paper/cardboard/sticker fabric, plastic surfaces, |
| DIGITAL PRINTING Ink jet (piezo, continuous, drop on demand) | Digital File | little / mediocre | Paper/cardboard/sticker fabric, plastic surfaces, |
| LETTER PRESS | Relief /photopolymer | large | Paper/cardboard/sticker |
| DRY OFFSET | Relief /photopolymer | mediocre / large | Paper/cardboard/sticker metal |

# References

1.Siegemund F. & Krauer T, (2004), Integrating Handhelds into Environments of Cooperating Smart Everyday Objects, in Proceedings 2nd European Symposium on Ambient Intelligence (EUSAI 2004), pp. 160-171, Eindhoven, The Netherlands, Springer-Verlag.

2. Spyridon Nomikos1, Anastasios Politis2, Jenny Darzentas3, Thomas Spyrou4, John Darzentas5. Exploring cross-media concepts for future packaging – Challenges for the printing industry.In Proceedings.32nd International IARIGAI  Conference .4-7 Sept 2005, pp319  -  331.

3. Glyn Holland, Peter Harrop and Raghu Das, (2005), The A to Z of printed and disposable Electronic, IDTechEx, Cambridge, UK.

4.Abbott DA. Packaging Perspectives. Kendall/Hunt, Dubuque, IA, 1989.

5.Hine Thomas . The total Package-ISBN780316 365468-Back Bay Books

6. Idtech  19-20/April/2005 Cambridge-Presentation, Harrop Peter-.[Operations in Smart Packaging.]

7. «The Future of Print”, study by Pira International and Prima corporation, Pira International, April 2000, Surrey UK

8. Karttunen S., Nikulin H. : «Content and metadata

management in the media production workflow”. Journal

of pre press and printing technology Pira international Ltd.

Vol. 5. March 1999 pp 3 – 8, Surrey UK.

9. Gorry, A. and Scott-Morton, M. (1971) A Framework for Information Systems, Sloan Management Review, 13, Fall 1971, 56-79

10.Sprague, R. H., Jr. and E. D. Carlson. Building Effective Decision Support Systems. Englewood Cliffs, N.J.: Prentice-Hall, Inc.: 1982.

11 YIT L. YAM,PAUL T. TAKHISTOV,JOSEPH MILTZ,Journal of Food Packaging,Vol.70,Nr.1,2005

13.Taoukis PS,Labuza TP.3003.Time-temperature indicators(TTIs).In:Ahvenainnen R,editor.Novel food packaging techniques.Cambridge U.K.:Woodhead Publishing Limited .pp 103-126.

14. The PHT Product Suite.-www.phtcorp.com/Solutions/product_suite.asp

15. Intelligent Inks. (Conductive Inks in Packaging Applications),Vienna Austria 8-9 November 2005

16. Electronic Smart Packaging Reports. IDTech, Raghu Das.,pp 10-18,Cambridge 2005.

17. (www.gaspian.org)-Article / Tracking everything, everywhere, Katherine Albrecht

18.MITs Auto-ID Center;Article represented in G.A.S.P.I.A.N.

(Consumers Against Supermarket Privacy Invasion and Numbering)- (www.gaspian.org).

19 Retail RFID Systems without Smart Selves-J.Lindsay,et.al.-.Publ.23/Dec./2003-Nov.7,2003.

20. The Association for Automatic Identification and Mobility.(www.aimglobal.org).

21.Cypak AB /2005.Smart, secure and connected solutions for time-tagged data capturing. Marie Wall, VP Business Development.IDTech-Printed Electronics.19-20/2005-present. Cypak AB

22. Electronic Smart Packaging. Reports. . IDTech, Raghu Das.,pp 7-8,Cambridge 19-20/April/2005.

23. METRO-Future Store.(www.future-store.org)

24.(www.rfid-weblog.com)

25.[RFID Privacy].The Microsoft Perspective ( Submitted to the Federal Trade Commission)as a follow-on to the Workshop on RFID: Applications and Implications for Consumers, June 21, 2004 /

26.[Peter Harrop]  [An Introduction to Smart Packaging Cambridge  IDTechEx 19-20/April/2005].

Author Biography.

Spyridon Nomikos received ,BA-in Technology of Graphic Arts in TEI of Athens and BSc from University of Middlesex  in 2001.Since then he has worked in research area on (Smart Packaging), in University of the Aegean, Dept. Product and Systems Design Engineering. He is Lecture in TEI-Graphic Arts Technology. Member TAGA, GATF.